## Slide 1: Pioneer A&W BT Stack Q&A (04/15)
Questions about A&W BT Stack for Suzuki Simple Radio H/U
Q1: If A&W's BT stack supports "A2DP" and "AVRCP" and provides M/W to control a BT-only HCI module, please provide an estimated ROM/RAM size.
A1: A&W's stack/profile supports Cortex M3/M4 MCUs and already implements HFP, A2DP/AVRCP/PBAP functions. It also provides simple and easy-to-use interfaces for upper-layer applications, along with sample code that can be directly applied, reducing development work. Based on this project's memory requirements, the estimated memory usage is as follows:
Q2: Suzuki have requested that the time be automatically corrected when pairing with Bluetooth devices, but Pioneer is currently unaware of a method for automatic time synchronization without using a dedicated smartphone app, and therefore has not been able to provide an answer.
If A&W has a method for automatic time synchronization other than Bluetooth LE TIP, please let us know.
A2: Yes, we have solutions for both BLE and Classic to synchronize the device with the phone‘s time. HCI type chips offer greater flexibility in functionality and usage based on customer needs. The memory used is as follows. For time synchronization, we offer two methods: BLE Tip and BT Classic. Neither case requires any special software or anything similar on the phone. Their memory usage is as follows:
Bluetooth A2DP Sink/AVRCP , MAP(Time sync) |  |  | 
Item | Code Size | RAM Size | CPU Loading
BT Stack | 100KB | 15KB | Negligible
A2DP Sink/AVRCP (Include SBC decode) | 12KB | 1.5KB | 30MHz
MAP(Time Sync) | 9KB | 1KB | Negligible
Total | 121KB | 17.5KB | 30MHz
Bluetooth A2DP Sink/AVRCP , BLE TIP |  |  | 
Item | Code Size | RAM Size | CPU Loading
BT Stack/BLE | 140KB | 15KB | Negligible
TIP |  | 3.5KB | Negligible
A2DP Sink/AVRCP (Include SBC decode) | 12KB | 1.5KB | 30MHz
Total | 152KB | 20KB | 30MHz
Bluetooth A2DP Sink/AVRCP |  |  | 
Item | Code Size | RAM Size | CPU Loading
BT Stack | 100KB | 15KB | Negligible
A2DP Sink/AVRCP (Include SBC decode) | 12KB | 1.5KB | 30MHz
Total | 112KB | 16.5KB | 30MHz

## Slide 2: Pioneer A&W BT Stack Q&A (04/15)
Questions about A&W BT Stack for Suzuki Simple Radio H/U
Q3: Pioneer is considering the NXP S32K3xx series (312?), and we would like to know if A2DP + AVRCP processing is possible with this MCU, and if you can provide an estimate of the CPU load, please let us know.
A3: Refer to A1 and A2
Q4: If Pioneer purchases the A&W BT M/W and Azure Wave's BT-only module (AW-BTA03: Automotive Grade) instead of the BT complete module, do they need to purchase them separately from each other? For PIO procurement, it's likely that, as before, the hardware (module) and BT stack will be quoted separately.
A4: A&W can accommodate either request, as per Pioneer's requirements.
Q5: What is the royalty image for a Bluetooth Stack with A2 specifications for a Bluetooth-only HCI module?
A5: Base on Suzuki project spec. the royalty image for the A&W BT Stack is around USD 0.35 .