## Slide 1: JKC A&W CP/AA Technical Roadmap Q&A (03/27)
A&W CarPlay/Android Auto Solution
End-to-End System-Oriented Design & Service:
- expedite development & ease certification process
  1. CarPlay & Android Auto SDK
      Connection Management: Authentication ( OOB, iAP2, MFi), Connection, Reconnection,
      Switching between Muti devices and Mirroring AP ( CP, AA…)
      Resource Management: Audio Focus / Mixing / Ducking Policy, Last User Mode: Native UI , CarPlay UI
      Solve User Input, UI Stream, Local GPS / GNSS (Blind guidance , Dead-Reckoning)
  2. Audio System:
      Driver : WiFi ( Throughput , Interference ,None DFS (Dynamic Frequency Selection) ),
      USB: Smart OTG (Role switch , Charging , USB Power Management)
      - System Configuration : Resampling, Jitter Buffer, Scheduling / Priority
      System Optimization : Fast Path , low Latency, RTD, Fast Cold Boot Connection
  3. Audio Quality
      ITU-T: Assist with resolving system-level problems (Bulk Delay, Sample Rate Mismatch, microphone sound dropouts…)
      Siri Speech Output Quality: Improves accuracy of speech recognition ( AEC, Leading Zero, Max Zero )
      ECNR / AEC : Provided by A&W : Auto Tuning Tool : Preemptively resolve software integration issues at an early stage

## Slide 2: A&W CarPlay Block Diagram
JKC A&W CP/AA Technical Roadmap Q&A (03/27)

## Slide 3: A&W Android Auto Block Diagram
JKC A&W CP/AA Technical Roadmap Q&A (03/27)

## Slide 4
JKC A&W CP/AA Technical Roadmap Q&A (03/27)
A&W PhoneLink Group Solution Diagram

## Slide 5: JKC A&W CP/AA Technical Roadmap Q&A (03/27)
A&W CarPlay/Android Auto Roadmap
Spatial Audio:
This feature requires an upgrade to CarPlay Plugin R18.1, which has been completed. A proof of concept (PoC) has been internally validated for 5.1-channel audio data transmission and decoding. The exported 5.1-channel PCM audio plays back successfully.
2. Apple AirPlay:
The AirPlay Video Specification for CarPlay Plugin R19 has not been released yet.
As attached file, AnW’s AirPlay Server is discoverable; iPhones can now connect and initiate screen mirroring or
streaming to the PC.

## Slide 6: JKC A&W CP/AA Technical Roadmap Q&A (03/27)
A&W CarPlay/Android Auto Roadmap
3. CarPlay Ultra
We are looking for a platform suitable for PoC (Proof of Concept) validation, which must address dependencies across the following layers:
Hardware and Connectivity Layer
MFi Certification: It is required to obtain Apple’s MFi authorization and the corresponding protocol stack code (Accessory SDK).
High-performance wireless connectivity: CarPlay Ultra essentially requires Wi-Fi 6 (802.11ax) and Bluetooth 5.x. Low latency is the top priority.
Multi-display interfaces: The EVB (Evaluation Board) must support multiple video outputs (e.g., LVDS, MIPI-DSI, or HDMI) to simulate multiple physical screens such as the instrument cluster and central display.
System Architecture Layer
Multi-screen rendering capability: A powerful compositor is required, capable of handling H.264/H.265 video streams from the mobile device and accurately distributing them across different display regions.
Low-latency video decoding: The hardware decoder (VPU) must support ultra-low-latency multi-stream concurrent decoding.
Vehicle Data Layer
CAN / Ethernet signal mapping: Unlike previous versions, the Ultra version requires access to real-time vehicle signals such as speed, battery/fuel level, coolant temperature, and tire pressure. During the PoC stage, these data must be converted via a simulator or real gateway into Apple’s required Vehicle Signal Specification (VSS) format.
Bi-directional control interface: It must support reverse control from the CarPlay UI to hardware functions such as air conditioning, seats, radio, etc.

## Slide 7: JKC A&W CP/AA Technical Roadmap Q&A (03/27)
Other:
Voice Bubble
In-cabin area is divided into several regions (bubbles).
Speech from other ‘bubbles’ will not be recorded by the microphone of that specific
region. For example, driver at region 1 is talking on the phone, while region 4
passenger is talking to another passenger simultaneously. Microphone at region 1
will collect only driver’s voice and send it to the far-end side party.
This will ensure each region’s communication quality.
DSP techniques and DNN processing are used to achieve this.
Voice Separation
When a microphone receives several voices simultaneously, this technology can separate each voice
so they will not interfere with each other.
This is the base technology of other technology like “Voice Bubble”.

## Slide 8: JKC A&W CP/AA Technical Roadmap Q&A (03/27)
Other:
3. Ethernet AVB
AVB is used to replace proprietary heavy wiring while upgrading standard Ethernet from best-effort to
a Time-Sensitive Network. It supports the high-bandwidth data required for modern Cockpit and ADAS
architectures. AVB is a collection of IEEE 802.1 standards—such as 802.1AS, 802.1Qat, and 802.1Qav
—plus the IEEE 1722 transport protocol. As illustrated in the sample architecture, Ethernet AVB facilitates
a distributed, scalable network that supports real-time audio and video streaming; it also leverages a ring
topology to ensure path redundancy for system robustness.
HU
Bridge
Bridge
Bridge

## Slide 9: JKC A&W CP/AA Technical Roadmap Q&A (03/27)
Q: Could you please describe the royalty image of A&W's total solution (CP/AA, ECNR, BT stack)?
A: The royalty image is less than US$1.5.