## Slide 1: ALPINE ITU-T TEST ECNR(Aftermarket) Q&A (01/21-23)
Questions about A&W ECNR(Aftermarket) for ALPINE
Q1: Purpose of the A&W ECNR config tool is to create ECNR parameters based on test results, but it cannot automatically create parameters based on test results. Is this understanding correct?
A1: Yes, it cannot automatically create parameters based on test results. But we have an Auto tuning tool to help reduce some major parameters tuning time, such as Bulk delay, Echo tail length, RES…
Q2: Does the A&W ECNR configuration tool have a way to send adjusted parameters to the ECNR module (S/W)?
A2: Currently this function is not available. We will consider it in future release.
Q3: In the future, ALPINE hope to realize a function that will allow the A&W ECNR configuration tool to read ITU-T TEST results (dump files), automatically adjust parameters for NG items, and output the results.
A3: We will consider it and study how to do it well. But due to its complexities it may not be available soon.
Q4: ALPINE would like to have a guidebook that lists what functions in the A&W ECNR config tool need to be adjusted for specific items that failed the ITU-T test.
A4: Please refer to attached ITUT tuning guide_2026_alpine.pdf.
Q5: ALPINE would like to have a document that describes the flow (recommended evaluation order and procedures) for performing each test using the A&W ECNR configuration tool.
A5: Please refer to attached ITUT tuning guide_2026_alpine.pdf, p.3.

## Slide 2: ALPINE ITU-T TEST ECNR(Aftermarket) Q&A (01/21-23)
Q6: As A&W ECNR, I would like to know if there are any recommended values ​​for the distance between the microphone and speaker (usually 55 cm) and the POD position during the ITU-T TEST.
A6: From SNR (Signal to noise ratio) point of view, it is suggested to keep the distance from the microphone to the HATS mouth as short as possible. Also a directional microphone is suggested to reduce noise pickup.
Q7: ALPINE would like to provide a document that explains each parameter in a text file after adjustment. The reason is that there are various parameter items, but it is difficult to know which ones should be adjusted and which ones users should not change.
A7: A&W does not recommend adjusting parameters directly in the text file. It contains many rarely used settings, which makes the modification process overly complex for users. We recommend adjusting (changing) parameters by the ECNR configuration tool ConfigTool.
Users could refer to Expert config tool ECNR parameters and Tuning Guide_v14_eng.pdf for each parameter’s meaning.
Q8: Similarly, it is unclear which values ​​can be changed by the user and which are internal adjustment items (not changeable) for each adjustment window. If possible, we would like you to consider ways to separate the user settings and internal settings windows.
A8: Users are suggested to adjust ECNR parameters by using ConfigTool. It included common used parameter settings for users. P.8~9 of Expert config tool ECNR parameters and Tuning Guide_v14_eng.pdf listed the parameters that users need to use during tuning. Other parameters are for ECNR internal use, users are not recommended to use them.

## Slide 3: ALPINE ITU-T TEST ECNR(Aftermarket) Q&A (01/21-23)
Q9: For the ECNR settings on iPhone FaceTime Audio, are the WB and other settings OK as they are? Or are special settings such as 24KHz sampling required?
A9: Facetime audio specification is the same as CP WB, so CP WB config file can be used without modification. But still a test call is suggested to make sure if Facetime audio path characteristics is the same as CPWB. As for sample rate, it depends on customer’s system design, it could be 24kHz, also could be other rate after conversion.
Q10: Echo Tail length needs to be changed depending on the vehicle model, so if you set a maximum length, can it be applied to all vehicles?
A10: It is not suggested to apply a maximum length Echo tail length to all vehicle cabins. Too long Echo tail length setting will not get an optimal performance.
Q11: Are the Rxin and EXT Refin values ​​in the config tool the same?
A11: Rxin is the signal from Bluetooth/CarPlay, while Ext. Refin is the actual signal being sent to speaker (e.g. DSP/Codec loopback).
Users should use actual Refin signal as simulation input for correct results.
Q12: Before providing ECNR to customers, does A&W ever request that they obtain (or borrow) the product (actual device) from the customer and evaluate it in advance?
A13: It is not a must. But A&W need to know the toolchain so we can build a workable library for customer’s HU.
Also we suggest customer can provide a test call recordings so that we can check if the HU system‘s audio path is ok or not.