## Slide 1: Infineon ECNR Q&A (02/06)
Questions about ECNR for Infineon (Yamamoto-san)
Q1: For the purpose of information exchange within Japan, Infineon Japan would like to conclude a local NDA in Japan (A&W and Infineon Japan).
A1: If Infineon Japan provides us with an NDA template, A&W will review the content and proceed with the NDA conclusion.
Q2: Please provide materials to introduce A&W ECNR to customers.
> A&W ECNR operating specifications: CPU load, ROM/RAM, etc. on ARM M55
> A&W ECNR DSP operation: ARM U55 compatibility, DSP load, ROM/RAM, etc.
> A&W ECNR basic functions: Quantum Bit support, sampling frequency support, etc.
> A&W ECNR supported functions: Beamforming, sound source separation, human voice extraction, etc.
A2:
A&W ECNR operating specifications: CPU load, ROM/RAM, etc. on ARM M55
Currently we have only the resources usage on ARM Cortex A53. We can measure it on M55 if we have M55 EV board and toolchain. Current ROM/RAM usage is 348kB/245kB for 16kHz sampling rate.
b. A&W ECNR DSP operation: ARM U55 compatibility, DSP load, ROM/RAM, etc.
Is U55 an NPU (Neural Processing Unit) instead of a general DSP.
A&W ECNR is based on DSP processing, it is possible to porting it to a DSP but cannot be ported to an NPU.
It is possible to port A&W ECNR to a Helium DSP. We can evaluate if it can be ported on Helium DSP if we have EVB, dsp porting guide, and development tools.

## Slide 2: Infineon ECNR Q&A (02/06)
Questions about ECNR for Infineon (Yamamoto-san)
c. A&W ECNR basic functions: Quantum Bit support, sampling frequency support, etc.
A&W ECNR support 16-bit resolution, 8/16/24/32/48kHz sampling frequency, 24ms TX processing latency.
Other detail functions please refer to attached datasheet.
d. A&W ECNR supported functions: Beamforming, sound source separation, human voice extraction, etc.
2-mic Beamforming is supported while sound source separation/human voice extraction is not supported currently.
A&W is developing a DNN-based NR. Sound source separation and human voice extraction are also under A&W planning. Could Infineon share more information with us about these technologies are used in what kind of applications and products?
Q3: Could A&W provide a sample of A&W ECNR running on Infineon's MCU (PSOC Edge E83)?
(M55 operation, U55 operation (if possible))
Infineon will provide the EVB and development environment.
A3: What kind of sample does Infineon want?
We can make an executable which can process an audio file and save processed audio to another file.

## Slide 3: Infineon ECNR Q&A (02/06)
A&W ECNR Ready & Development List
The A&W ECNR themes that are already in mass production or are under development are listed below.
If there are any themes that MCU customers are particularly interested in, please let us know and we will consider prioritizing their development.