## Slide 1: Pioneer ECNR(Nureki-san) Q&A (11/05)
Q1: Is it possible for A&W to provide a similar in-vehicle evaluation in September 2024 that would exceed the score
given by PIO and earn a Pass (3.5 or higher) rating?
Ans1: Following are the two proposals for PIO ECNR evaluation:
Proposal 1: On-site
Prepared a Car at PIO JP site.
Speaker and Mic: Prepared by A&W.
A&W send an engineer to PIO site co-work.
If some score is not good, A&W engineer can discuss with PIO and adjust parameters based on the test results.
Proposal 2:
Prepared a similar in-vehicle evaluation at A&W TWN site
Step a (A&W tuning):
  . Kinno-san calls from JP office to TW in-car (simulate PIO test scenarios)
  . TW engineer tune based on the call recordings
  . Kinno-san calls from JP to TW again. Check the results.
  . If the results are good, send the recordings files to PIO for comments.
  . Adjust ECNR parameters according to PIO’s comments, if any.
Step b (PIO evaluation):
  . Kinno-san goes to PIO office, call to TW in-car, then PIO test and evaluate.
  . A&W will reserve the test call recordings. A&W can analyze the unsatisfied test results.

## Slide 2: Pioneer ECNR(Nureki-san) Q&A (11/05,19)
Q2: Is it possible for A&W ECNR to accommodate specification changes requested by PIO?
Ans2: Customization for better suiting PIO's spec/requirements is always our policy.
Q3: PIO heard that A&W's ECNR supports two microphones, but what is the assumed distance between the microphones?
If there are any restrictions on the distance between the microphones, please let me know.
Ans3: 2-mic Beamforming is designed to improve the recognition rate of an ASR (Automatic Speech Recognition).
The range of min. and max. of microphone distance is from 1cm ~ 10cm, but the commonly used mic distance range is from 1cm ~ 2cm for sampling rate greater than 16kHz.