## Slide 1: Alpha Theta Corporation A&W BT Stack Lite Q&A (10/20)
Q7: When Alpha theater considers the A&W Command Line Solution, we are concerned about the ROM/RAM and CPU load of the system CPU.
※If the CPU performance is insufficient, considering the above chip will increase costs.
Please estimate the ROM/RAM capacity and CPU load if the same BT specifications (including LE-Audio) as the Silex Wifi/BT Module are achieved with a command line solution.
※Alpha theater biggest concern is whether the LC3 coding/decoding (M/W) will be able to withstand the system demands.
A7: ARM Cortex M7 LC3 CPU usage estimation (based on measurements from Cortex A53):
Audio format: 160kbps stereo 48kHz
 | LC3 Decoder | LC3 Encoder
CPU (MHz) | 106 | 186
RAM (KB) | 53 | 32
ROM (KB) | 84 | 103