## Slide 1: JKC A&W BT Stack Introduction Q&A (10/03)
Questions about A&W BT Stack for JKC
Q1: What kind of solutions and services does A&W offer with its CP/AA?
A1 Specific platform (ex., TCC 8050, MTK 2718,...) has been set up with complete related Apps and system to do:
1. Simulating the resources occupation between other Apps and CP/AA to make sure correct resources allocation,
switching, audio mixing, latency…
2. Simulating the switching among different devices, like, CP, AA, Bluetooth…
3. Performance optimization, including connection / reconnection speed and latency tuning like RTD
4. Audio quality pre-tuning to facilitate ITU-T certification
5. Pre-testing for Facet and PCTS items
6. IOP for different mobile OS / model and APPs
Q2: From A&W's perspective, what is the current status of LE-Audio(BLE) (mobile phones and products)?
Also, how do you view the life of classic products?
A2: 1. We can’t see the intention for Apple to support LE Audio and other 3 parties’ high quality audio codec (ex., AAC, LDAC, apt-X)
can’t be used.
2. Life of classic products: LE Audio can’t totally replace unless Apple and other high quality audio quality codec support it.
3. While, our customers still adopt LE Audio to do multi audio playing with less BT chips.

## Slide 2: JKC A&W BT Stack Introduction Q&A (10/03)
Q3: How much difference is there in current consumption between BT Classic and LE-Audio (BLE)?
JKC heard that when streaming music with BLE, the current consumption is about the same as with Classic.
Is this true?
A3: . Power consumption: when in audio streaming, not much difference for Classic and LE Audio
Q4: BT chip supports dual mode, but is it possible to switch between BT Classic and LE Audio (BLE) with a single BT module?
If so, is the switching smooth?
How long does it take to switch?
(An example or demo measurement would be fine)
A4: For switching modes, the procedure is to disconnect one mode, then connect to the other mode.
The switching time is around 200ms-500ms, some difference among different BT chips.
Use scenario in mobile phone side is to mostly let user select which mode will be used.