## Slide 1: KC26 8 inch (USB connection) RTD problem Q&A
Regarding KC26 8 inch (USB connection) RTD problem
1. This issue was disclosed to us on June 2nd when A&W visited to support Alengo ECNR (VCP Tool) for ITU-T TEST.
2. A&W responded that the Alengo ECNR delay time is fixed at 48msec in total, 24msec for transmission and 24msec for reception (not affected by data or parameters), and showed understanding of JKC.
3. At the time, the RTD measurement value exceeded the specifications by about 200msec, so the ECNR delay time was not noticed.
4. On July 18th, JKC Mr. Tuchida reported the latest RTD as follows.
RTD specification: 275msec, latest measurement value: 379.49msec, difference: 104.49msec
※Details are below.
5. JKC has requested the following support from A&W (Tayler) and JKC is waiting for a response.
> Arengo presents a way to reduce the delay time of ECNR without degrading its performance.
> Neusoft presents advice on reducing the delay time of system S/W.
6. In my opinion, Neusoft has presented the following possibility of reducing the delay time of system S/W, but I think that the details need to be confirmed.
①ECNR的变更， VCP bin 2 => 11
②pcm period count和 period size变更 512 * 2
③mic流每次mic读取数据量变更 48ms数据=> 8ms数据
④Setup Respons(Audio时)发送时机延后，收到setup的70ms后返回。
> Does ① not match our view?
> What is the impact of ② and ③ on ECNR?
> Details of ④ are unknown?
7. What's even more puzzling is that the RTD measurement results vary by nearly 100 msec.
(The range is from about 370 msec to about 470 msec.)