## Slide 1: A&W Bluetooth Stack - PhoneLink SDK
Key Advantages – Customized for Your Application
Service & Support — Included with Your License
A&W’s Bluetooth stack is engineered for mission-critical connectivity. Trusted by automotive Tier-1/OEM and deployed in hundreds of millions of units worldwide, it delivers a proven, reliable foundation for your next-generation devices from automotive and IoT to consumer applications.
Lifetime technical support & maintenance
IOP test service for mass production
Support for Bluetooth Certification including pre-PTS test
Optimized for resource-constrained systems
Best interoperability.
Anti-hacking attack, verified with Static & Fuzzing tests
Support LE Audio including LC3 Encoder/Decoder
Supported NXP BT/Wi-Fi :
AW 693/692
AW 611
IW 611/612
AW 690
88Q9098
88W8987
88W8887
88W8787
FreeRTOS
eT-Kernel
µlTRON
ThreadX
uC/OS2
Android
Linux
QNX
Supported OS:
A&W Bluetooth Stack is also fully compatible with other NXP BT/Wi-Fi chips

## Slide 2: Memory Footprint
SDK |  | RAM (kB) | ROM (kB) | CPU loading (MIPS) | REMARK
BT 5.4 Stack with Classic Profiles |  | 35 | 218 | 30 | 30 MIPS for A2DP SBC; Excluding playback jitter buffer HFP HF&AG, A2DP SRC/SNK, AVRCP CT/TG, PBAP PCE, SPP Include 30KB memory buffer
BLE Only Stack |  | 46 | 115 | Negligible | Pure BLE Stack Include 34KB memory buffer
LE Audio Profiles (Support all roles) |  | 71 | 68 | Negligible | Excluding playback jitter buffer and CODEC Include 30KB memory buffer
LC3 Encoder |  | 30 | 110 | 95 | 48K, one channel
LC3 Decoder |  | 44 | 107 | 53 | 48K, one channel
Noise Reduction | 8K | 56.8 | 176 | 36 | 
 | 16K | 111.2 | 176 | 60 | 
The figures provided in the below reference table represent general use cases. For cost-sensitive or resource-constrained systems, we can significantly reduce memory footprint through optimization based on customer requirements.
LC3 Codec ROM
149KB