## Slide 1: Q&A
Q: A&W Bluetooth initial time longer than Native Bluetooth
A:

## Slide 2: Q&A
Q: When a mobile device is connected to HU, the Bluetooth AVRCP metadata is “unknown”. In our Bluetooth Player, we are not able to see the song metadata, and AVRCP control ( play, pause, next ) is not available.
A: We analyzed the native API they used and compared it with the AAOS native API version we are currently compatible with. we currently support a lot newer API versions than they use, and there are some old APIs or define that we don't use, so we'll arrange time to add those APIs.

## Slide 3: Q&A
Q: A&W CTS experience
A: A&W's Japanese customers have already passed CTS verification and are using A&W's Bluetooth.

## Slide 4: Q&A
Q: Regarding multi connection/streaming what features are feasible for Smart Cockpit(CYW89373) and Smart AC (NXP AW692) devices?
A:
No. | BT Advanced Feature | CYW89373 | AW693
1 | Multi-connection: Mobile + Headset + BLE devices | OK | OK
2 | Driver & Passenger simultaneous play: A2DP SNK + SRC | OK | OK
3 | Playback of different A2DP sources : A2DP SRC + SRC | OK | OK
4 | 2 SCO | OK | OK
5 | HFP ( SCO ) + LE Audio (2 CIS) | NA | Ok for AW611 ; AW693 most likely no problem.
6 | A2DP SNK + LE Audio (2 CIS) | NA | Scheduled to be tested end of Dec.
7 | 4 CISs | NA | Ok for AW611 ; AW693 most likely no problem.